UNITY AND DISCIPLINE

NCC DTE (TN,P & AN) CHENNAI

‘C’ CERTIFICATE EXAMINATION

SPECIAL SYLLABUS SIGNALS ARMY WING (SD/SW) 2010-2011

MODEL QUESTION PAPER-II

Special Subject

_________________________________________________________________________

SER NO							TOTAL MARKS : 110

ROLL NO :							TIME ALLOTTED : 1 Hrs

_________________________________________________________________________

( FOR OFFICE USE ONLY)

| Srl No | Subject | Marks Allotted | Obtained | Sig of Evaluator Obtained |
| --- | --- | --- | --- | --- |
| 1. | Organisation of Signals | 08 |  |  |
| 2. | Radio Equipment | 16 |  |  |
| 3. | Line Equipment | 19 |  |  |
| 4. | RT Procedure | 18 |  |  |
| 5. | Signals Centre Procedure | 12 |  |  |
| 6. | Flag Drill | 04 |  |  |
| 7. | Troposcatter | 21 |  |  |
| 8. | Charging Set | 05 |  |  |
| 9. | Construction of Line Equipment | 07 |  |  |
| Total | 110 |  |  |

General Instructions :-

1. Read all the questions and clarify doubts before answering .

2. All answers to be written on the Question Paper next to each Question at the space given

for the same

3.  Only Ballpoint pen to be used for writing the answer any cutting or over writing in (T/F)               Question will be marked as Zero.

4. No additional answer sheets or additional time will be given under any circumstances .

5. Criteria to pass 45% in each subject and 50% in aggregate.

________________________________________________________________________________                                                             	1.	Organisation of Signals							Marks-08

(a) Fill in the blanks 		                                                                       	Marks- 03

    - The RR Sec comes under 2 Coy Coy in a Div Signal Regt.

    - The responsibility of Signal centre in Sig Regt is that of 2 i/c  Coy

    - Bde Sig Coy is responsible to provide all types of communication down to Bn HQ

(b) Write full form                                                               			Marks:-05

(i)	ALU – (Arithmetic Logic unit)

(ii)	MHZ- Megahertz

(iii)	TM – Technical Maintenance

(iv)	VHF- Very High Frequency

(v)	CPU – Central Processing Unit

-2-

2.		Radio Equipment		     						Marks-21

(a) Fill in the blanks					     			Marks-07

(i)	There are 920 Channels in ANPRC -25

(ii)	The frequency Range of RS Motorola GP 338 in VHF Range is                            	136 Mhz to 174 Mhz

(iii)	Human hearing frequency is 20 Hz to 2000 Khz

(iv)	VHF frequency range is from 300 MHz to 3000MHz

(v)	There are Three types of channels used for the transmission.

(vi)	The frequency range of AN PRC-25 is fixed in 2 bands.

(vii)	The power O/P of Radio set GP 338 is 5 Watt in VHF.

(b) Chose the correct answer.						Marks-04

(i)	FM Stands for	?_____________ (Frequency modulate, Frequency modulation, Frequency module)

(ii)	The maximum Comn range of Radio set GP-338 Motorola with repeater is ___ Kms.       (40 Kms, 35 Kms, 45 Kms)

(iii)	Microwave transmission consists of High frequency waves in the range of  	______________	(100-300 MHz, 1000-3000MHz,10,000-30,000MHz)

(iv)	_______________Aerial is used for ground wave communication

(Rod, Ribbon,  Wire)

(c) True/False									Marks-04

(i)	Communication satellites are placed in geo Synchronous orbit. True.

(ii)	Radio set AN PRC 25 is a VHF Radio set which can be used for comn. True.

(iii)	Radio set ANPRC 25 is used at platoon & company level for communication. True.

(iv)	Effective range of communication of Radio set AN PRC-25 without            	booster is 25 (Kms). False

(d) Write Short Answer							Marks-06

(i)	What is PROM?

PROM is an acronym for programmable read only memory. A PROM is a memory  chip on which data can only be written once and once it is written it remains there forever.

(ii)	What are the differences between cellular Mobile Telephone & Cordless 	Telephone?

Cellular Phone 			                     	Cordless phone

(aa)	Provide large coverage area	(aa)	Applicable with in limited 										coverage area

(ab)	Limited traffic handling 	(ab)	High traffic handling

(ac)	Roaming is applicable		(ac)	Roaming is not applicable

(ad)	Cellular is cordless 		(ad)	Cordless is not Cellular

(iii)	What do you mean by up –link and down –link?

In a Satellite all the ground equipment along with transmission path and receiving antenna at the Satellite are included in up- link system.  The down link is Satellite transmitter out put power, downlink antenna gain and beam width.

3.		Line Equipment 								Marks-20

(a) Fill in the blanks                                                                         		Marks-07

(i)	FAX is a common short form of Facsimile

(ii)	Series connection can be used in Auto Exchange.

(iii)	Three types of universal junctions are used in SWBD 17 line exchange.

(iv)	There are Two types of line parties.

(v)	In a fibre optic cable the core is surrounded by a second layer of glass called Clad.

(vi)	In telephone set 5 B/5A 3 Volt dry Bty is used.

(vii)	Teleprinter is Line equipment.

(b) Write full form								Marks-04

(i)	TCP – 		Transmission Control Protocol

(ii)	FTP- 		File Transfer Protocol

(iii) 	PPP - 		Point to Point Protocol

(iv)	H T T P – 	Hyper Text Transfer Protocol

(c) True/ False								            Marks-03

(i)	Dialing facility is provided in Telephone Set 5B. False

(ii)	15 line Exchange is a portable. True.

(iii)	The core of a fibre optic cable is a very thin strand of highly refined cylindrical 			                         glass. True.

(d) Write short answer							Marks-06

(i)	What is an ‘E’ Mail?

E-mail is an electronic message sent from one computer to another computer you can

send and receive personal and business related messages with attachment like pictures

or other documents.

(ii)	What does ISDN Stand for ?

Integrated Services Digital Net Work.

4.		RT PROCEDURE								Marks-20

(a) Fill in the blanks								Marks-05

(i)	In RTG Morse code can be used for passing massages.

(ii)	There are Four  types of calls in communication net work.

(iii)	The maximum time taken to clear a flash message is 15 Minutes

(iv)	B-1 Link provides Radio communication between Bde Hq and Bn Hq.

(v)	Rules of Radio telephone are RSVP

(b)Write the correct answer							Marks-05

(i)	RTG stand for ________________________

(Radio telegraphy, Radio Tele Communication graphy, Radio Tele            					printer graphy)

(ii)	______ is a secret group of three letters used to cancel the identity of the 	formation / Unites during transmission.  		 	  	
 	(Code sign, Address, Call sign)

(iii)	What is the number of message form _____________

(IAFU 4009,	 IAFU 4002,	 IAFU 4001)

(iv)	There are ___________ types of VFT.

( 6, 	5,	4 )

(v)	A message of over 50 words or groups is called as __________ message	            		( Short message, Long message, Medium message )

(c) Write full forms								Marks-04

(i)	DNA      - Distance Number Not available

(ii)	TIDEX   - Time division Electronic Exchange

(iii)	ISD         - International subscriber dialing

(iv)	ONA       - Originator Not Available

(d)  Write short notes							Marks-06 					(i)	What do you understand by UNICODE?

It is a simple code used to convert the grid reference to a coded form. It is 				changed daily.

(ii)	What is the basic principle of Radio Telephony?

Brevity,  Accuracy,  security and  speed.

5.		SIGNAL CENTRE PROCEDURE						Marks-08

(a) Fill in the blanks								Marks-03					(i)	There are Two types of signal centres.

(ii)	There are Two  types of staff working in Signal Centres.

(iii)	Immediate message is denoted by the letter  OP.

(b) True/False								Marks-03

(i)	The clearance clerk will close the Signal Centre register at 2359h daily. True .

(ii) 	On duty DSO is responsible for Signals Centre complex. True.

(iii)	LTR means Line Test Recorder True.

(c) Write Short Note								Marks-02

(i)	Name the types of messages?

There are 6 types of Messages

(a)	 Flash Message		(d)	Priority Message

(b)	Emergency Message		(e)	Routine Message

(c)	OP-immediate Message	(f)	Deferred Message

6.	Flag Drill									Marks-05

(a) Write the Appointment codes of the following				Marks-02

(i)	EME Advisor	- Eagle										(ii)       Air Force Rep- Hawak

(iii)	Quarter Master- Panther                                                                                                      	(iv)	Commanding Officer- Tiger

(b) What is the difference between modern and old communication system (Marks-03)

Modern communication 				Old Communication

(i).  Fiber-optical, Radio, troposcatter, satellite,          (i) Line, animals, Birds, Flags,

andcomputer are used   				     Men, DR, Messenger are   used

7.	Troposcatter 									Marks-18

(a) Fill in the blanks								Marks-06

(i)	The range of troposcatter communication is from 70 Kms to1000Kms.

(ii)	The lower layer of the atmosphere below 15 Kms height is called Troposphere 	region.

(iii)	The first artificial satellite launched by USSR was Sputnik.

(iv)	The communication Satellites are placed in orbits called Equatorial                          geosynchronous orbit.

(v)	The name of first satellite launched by India was Arya Bhatta

(vi)	The first Indian to go to space is Wg Cdr Rakesh Sharma

(b) True/False								Marks-03

(i)	The first man go to the space Yuri Gagari of Russia. True.

(ii)	Troposcatter communication provides 32 Telegraph / Telex channel. True.

(iii)	Communicating Satellites are placed at an attitude of approx 36,000 Kms. True.

(c) Write Short Answer							Marks-09

(i)	Name five satellites according to their functions.

(aa)	Navigation Satellite

(ab)	Weather Satellite

(ac)	Communication Satellite

(ad)	Military Satellite

(ae)	Scientific Satellite

(ii)	Write down the application of troposcatter communication.

It is used for long range point to point communication ideal for rugged 			terrain mountain desert etc. It has following channel capacity Voice 			24,Telegraph 32,Data 03.

(iii)	Write Five Major components in a Satellite.

(aa)	The Transponder	(ad)	The control & Information System

(ab)	The Antenna		(ae)	The Rocket thruster System

(ac)	The Power Package

8.	Battery Charging								Marks-05

(a) Fill in the blanks								Marks-02

(i)	The electro chemical process in which liquid undergoes chemical                    decomposition as a result  of passage of electric  current is called Electrolyte

(ii)	Hydrometer is used to measure specific gravity in a secondary Battery

(b) Write Short Note								Marks-03

(i)	Name any three types of charging.

There are six types of charging

(aa) 	Initial charge 		(ad) 	Trickle  charge

(ab)	 Float charge 		(ae)	Gases charge

(ac)	 Normal charge 	(af)	Fresh charge.

9.	Line  Maintenance								Marks-05

(a) Fill In The blanks							Marks-03

(i)	JWD consists of Steel Wires.

(ii)	50000 channels can be carried in half inch diameter fiber optic cable

(iii)	Carrier quad are Two pair lines.

(b) Write Short Note     							Marks-02

(i)	What are the essential items used for line maintenance.

(aa)	Cutting plier 		(ad)	 Multimeter

(ab)	Insulation tape 	(ae)	 Screw driver

(ac)	 Axes 			(af)	Knife

UNITY AND DISCIPLINE

NCC DTE (TN,P & AN) CHENNAI

‘B’ CERTIFICATE EXAMINATION

SPECIAL SYLLABUS SIGNALS ARMY WING (SD/SW) 2010-2011

PRACTICAL MODEL QUESTION PAPER

Special Subject

| S/No | SUBJECT | MARKS |
| --- | --- | --- |
| 1. | Radio Equipment | 05 |
| 2. | Line Equipment | 05 |
| 3. | R T Procedure | 15 |
| 4. | Battery Charging | 05 |
| 5. | Line Construction | 05 |
| 6. | Flag Drill | 05 |
|  | Total | 40 |

Radio Equipment										Marks-05

Q1.	What is the full form of LED?

Ans.	Light Emitting Diode

Q2.	How many types of satellites are there and name them?

Ans.	Two types-(i) Active (ii) passive

Q3.	How many types of communication are there and name them?

Ans.	Two types of communication-(i) Radio comn (ii) Line comn.

Q4.	What is the frequency range of HF communication?

Ans.	3 to 30 MHz

Q5.	What is the function of aerial?

Ans.	To convert electrical energy into electro magnetic waves.

Line Equipment										Marks-05

Q1.	What is the input voltage of SWBD 15 line exchange?

Ans.	Internal-9V (6 x 1.5V)

External-6V (Secondary)

Q2.	What is the function of coupling jack?

Ans.	To connect two 15 line exchange to increase the capacity.

Q3.	What are the parts of line cord?

Ans.	Tip, Ring, Slave

Q4.	How many universal junctions used in SWBD 15 line?

Ans.	Three

Q5.	What is the function of external telephone terminal?

Ans.	When operator handset goes faulty it can be used as a operator handset.

.

R T Procedure											Marks-15

Q1.	How many types of Signal centre are there? Name them?

Ans.	Two types (i) Large Signal centre (ii) Small Signal centre

Q2.	How many types of message system are there? Name them?

Ans.	Two types (i) Normal system (ii) File copy system

Q3.	How many types of forms used in Signal centre? Name them?

Ans.	Two types of form used in Signal centre – (i) NR Sheet-IAFU-4020

(ii) Message form-IAFU-4009

Q4.	How many types of precedence are there?

Ans.	6 types.

Q5.	How much time is taken to clear a flash message?

Ans.	15 minutes.

Q6.	Give the full form of RT and RTG?

Ans.	RT-Radio Telephony, RTG-Radio telegraphy.

Q7.	How many types of calls used in RT? Name them?

Ans.	Three types (Single call, multiple call and Net call)

Q8.	What are the basic principles of radio telephony?

Ans.	B-Brevity, A-Accuracy, S-Security, S-Speed.

Q9.	What is radio net?

Ans.	Number of radio set working on the same frequency to communicate on another called radio 		net.

Q10.	What do you mean by DEO and DSO?

Ans.	DEO-Duty Exchange Officer and DSO-Duty Signal Officer.

Battery Charging										Marks-05

Q1.	Name the types of battery charging?

Ans.	Initial, Normal, Float, Trickle, Gassing and Freshing.

Q2.	Name the eqpt used in charging room?

Ans.	Charging set, Hydrometer, Volt meter and Shorting lead.

Q3.	Enumerate the defects of secondary battery?

Ans.	Sulfation, Buckling and creaking, Loss of active material, internal short cct.

Line Construction										Marks-05

Q1.	What is the strength of line party?

Ans.	1+9

Q2.	Types of line faults?

Ans.	Open faults, Short fault and loose fault.

Flag Drill											Marks-05

Q1.	Appointment code of 2IC and Signal adviser?

Ans.	2IC-Lamb and Signal adviser-Sparrow.

Q2.	Phonetic Alphabets?

Ans.	A-ALPHA, H-HOTEL, R-ROMEO, W-WHISKY