UNITY AND DISCIPLINE

NCC GP HQ COIMBATORE

‘B’ CERTIFICATE EXAMINATION

SPECIAL SYLLABUS ARMY WING (SD/SW) 2010-2011

MODEL QUESTION PAPER-II

Special Subject

_________________________________________________________________________

SER NO							TOTAL MARKS : 110

ROLL NO :							TIME ALLOTTED : 1 Hrs

_________________________________________________________________________

( FOR OFFICE USE ONLY)

| Srl No | Subject | Marks Allotted | Obtained | Sig of Evaluator Obtained |
| --- | --- | --- | --- | --- |
| 1. | Organisation of Signals | 08 |  |  |
| 2. | Radio Equipment | 21 |  |  |
| 3. | Line Equipment | 20 |  |  |
| 4. | RT Procedure | 20 |  |  |
| 5. | Signals Centre Procedure | 08 |  |  |
| 6. | Flag Drill | 05 |  |  |
| 7. | Troposcatter | 18 |  |  |
| 8. | Charging Set | 05 |  |  |
| 9. | Construction of Line Equipment | 05 |  |  |
| Total | 110 |  |  |

General Instructions :-

1. Read all the questions and clarify doubts before answering .

2. All answers to be written on the Question Paper next to each Question at the space given

for the same

3.  Only Ballpoint pen to be used for writing the answer any cutting or over writing in (T/F)               Question will be marked as Zero.

4. No additional answer sheets or additional time will be given under any circumstances .

5. Criteria to pass 45% in each subject and 50% in aggregate.

_________________________________________________________________________________                                                             	1.	Organisation of Signals							Marks-08

(a) Fill in the blanks 		                                                                       	Marks- 03

(i)	The responsibility of Signal centre in Sig Regt is that of 1 Coy

(ii)	The training schedule is prepared by 2 i/c.

(iii)	The responsibility of line sec is that of  1 Coy

(b) Write full form                                                               			Marks:-05

(i)	MT – Mechanical Transport

(ii)	CHQ- Coy HQ

(iii)	TM – Technical Maintenance

(iv)	RHQ- Regt HQ

(v)	QM- Quarter Master

2.		Radio Equipment		     						Marks-21

(a) Fill in the blanks					     			Marks-07

(i)	HF Frequency Range is from 3 MHz to 30 Mhz

(ii)	The frequency Range of RS Motorola GP 338 in VHF Range is                            	136 Mhz to 174 Mhz

(iii)	Human hearing frequency is 20 Hz to 2000 Khz.

(iv)	Human talking frequency range is 20 Hz to 4000 Khz.

(v)	There are Three types of channels used for the transmission.

(vi)	The frequency range of AN PRC-25 is fixed in 2 bands.

(vii)	The power O/P of Radio set GP 338 is 5 Watt in VHF.

(b) Chose the correct answer.						Marks-04

(i)	The area covered by more than one cellular organization is called 	_____________ ( Roaming, Locating , Hand Set off )

(ii)	The maximum Comn range of Radio set GP-338 Motorola with repeater              	is _______________________ Kms.     (40 Kms, 35 Kms, 40 Kms)

(iii)	The complete owner ship by a single organisation is the characteristic of 	______________________	(work station, LAN, WAN)

(iv)	_______________Aerial is used for ground wave communication

(Rod, Ribbon,  Wire)

(c) True/False									Marks-04

(i)	The geosynchronous satelight are based at the height of 3600 Kms. False

(ii)	Radio set AN PRC 25 is a VHF Radio set which can be used for comn. True.

(iii)	Radio set ANPRC 25 is used at platoon & company level for 	communication. True.

(iv)	Effective range of communication of Radio set AN PRC-25 without            	booster is 25 (Kms). False.

(d) Write Short Answer							Marks-06

(i)	What is jamming?

Jamming is the circuit of sending own Radio Signals with a view to make the strength 	net ineffective .

(ii)	What are the differences between cellular Mobile Telephone & Cordless 	Telephone?

Cellular Phone 				Cordless phone

(aa)	Provide large coverage area	(aa)	Applicable with in limited 										coverage area

(ab)	Limited traffic handling 	(ab)	High traffic handling

(ac)	Roaming is applicable		(ac)	Roaming is not applicable

(ad)	Cellular is cordless 		(ad)	Cordless is not Cellular

(iii)	What are the classifications of frequency?

VLF, LF, MF, HF, VHF, UHF, SHF, EHF,

3.		Line Equipment 								Marks-20

(a) Fill in the blanks                                                                         		Marks-07

(i)	In FAX system light beam passes through two Convex lenses to eliminate the scanning area

(ii)	Series connection can be used in Auto Exchange.

(iii)	Calling/ Answer plug is used in magneto Exchange.

(iv)	Subscriber is Indirectly connected in magneto telephone.

(v)	HLR switch consists of three position in telephone set 5 B

(vi)	In telephone set 5 B/5A 3 Volt dry Bty is used.

(vii)	Teleprinter is Line equipment.

(b) Write full form								Marks-04

(i)	TCP – 		Transmission Control Protocol

(ii)	FTP- 		File Transfer Protocol

(iii) 	PPP - 		Point to Point Protocol

(iv)	H T T P – 	Hyper Text Transfer Protocol.

(c) True/ False								Marks-03

(i)	Dialing facility is provided in Telephone Set 5B. False

(ii)	15 line Exchange is a portable.  True

(iii)	In tele phone Set 5 B Bell Alarm facility is provided. True.

(d) Write short answer							Marks-06

(i)	What is an ‘E’ Mail?

E-mail Is an electronic message sent from one computer to  another computer you can send and receive personal and business related messages with attachment like pictures or other documents.

(ii)	Difference between Tele Set 5A and 5B

Tele Set 5A 					Tele Set 5B

(aa)	Bell is pipe type 		(aa) 	Bell is saucer type

(ab)	Auto dial can be fitted 	(ab)	Auto dial can not fitted

(ac)	Line terminal spike tape	(ac)	Line terminal spring types

(ad)	Circuit is complicated 	(ad)	Circuit is simple.

4.		RT PROCEDURE								Marks-20

(a) Fill in the blanks								Marks-05

(i)	There are Four  types of calls in communication net work.

(ii)	The expanded form of Fax is Facsimile.

(iii)	The call made for a particular station is Single Call.

(iv)	B-1 Link provides communication between Bde Hq and Bn Hq.

(v)	Rules of Radio telephone is RSVP.

(b)Write the correct answer							Marks-05

(i)	RTG stand for ________________________

(Radio telegraphy, Radio Tele Communication graphy, Radio Tele            					printer graphy)

(ii)	______ is a secret group of three letters used to cancel the identity of the 	formation / Unites during transmission.  		 	  	
 	(Code sign, Address, Call sign)

(iii)	What is the number of message form _____________

(IAFU 4009,	 IAFU 4002,	 IAFU 4001)

(iv)	There are ___________ types of VFT.

( 6, 	5,	4 )

(v)	A message of over 50 words or groups is called as __________ message	            		( Short message, Long message, Medium message )

(c) Write full forms								Marks-04

(i)	So-in-C       - Signal Officer in- Chief

(ii)	TIDEX        - Time division Electronic Exchange

(iii)	ISD              - International subscriber dialing

(iv)	ONA            - Originator Not Available

(d)  Write short notes							Marks-06 				(i)	What is the need for radio procedure?

(a) 	Message can be passed and received systematically

(b)	Message can be cleared speedily so time can be saved

(c)	Security is possible

(d) 	Brevity and accuracy is possible.

(ii)	What is the basic principle of Radio Telephony?

Brevity,  Accuracy,  security and  speed.

5.		SIGNAL CENTRE PROCEDURE						Marks-08

(a) Fill in the blanks								Marks-03				(i)	There are Two types of signal centres

(ii)	There are Two types of staff working in Signal Centres.

(iii)	_______ time is taken for clearance of Flash messages.

(b) True/False								Marks-03

(i)	Time of released is filled in message form by the OC unit.  False.

(ii) 	On duty DSO is responsible for Signals Centre complex. True

(iii)	LTR means Line Test Recorder. True.

(c) Write Short Note								Marks-02

(i)	Name the types of messages?

There are 6 types of Messages

(a)	 Flash Message		(d)	Priority Message

(b)	Emergency Message		(e)	Routine Message

(c)	OP-immediate Message	(f)	Deferred Message

6.	Flag Drill									Marks-05

(a) Write the Appointment codes of the following				Marks-02

(i)	Air Force Rep - Hawak

(ii)	Quarter Master  - Panther

(b) What is the difference between modern and old communication system (Marks-03)

Mordern communication 				Old Communication

(i).  Fiber-optical, Radio, troposcatter, satellite,	(i) Line, animals, Birds, Flags,

and computer are used   				     Mans, DR, Messenger are     									     used .

7.	Troposcatter 									Marks-18

(a) Fill in the blanks								Marks-06

(i)	The range of troposcatter communication is from 70 Kms to1000Kms

(ii)	The lower layer of the atmosphere below 15 Kms height is called Troposphere 	region.

(iii)	The first artificial satellite launched by USSR is Sputnik

(iv)	The no of voice channels of troposcatter communication are 24.

(v)	The name of first satellite launched by India was Arya Bhatta

(vi)	The first Indian to go to space was Wing Cdr Rakesh Sharma

(b) True/False								Marks-03

(i)	The first man go to the space Yuri Gagari of Russia. True.

(ii)	Troposcatter communication provides 32 Telegraph / Telex channel. True.

(iii)	Artificial satellite revolving around the earth is called Geostationary 	Satellite. False.

(c) Write Short Answer							Marks-09

(i)	Name five satellites according to their functions.

(aa)	Navigation Satellite

(ab)	Weather Satellite

(ac)	Communication Satellite

(ad)	Military Satellite

(ae)	Scientific Satellite.

(ii)	write down the application of troposcatter communication.

It is used for long range point to point communication ideal for rugged 		terrain mountain desert etc. It has following channel capacity Voice 		24,Telegraph 32,Data 03

(iii)	Explain satellite communication.

A Radio communication service between earth station at specified fixed 		point when one or more Satellite are used.

8.	Charging Set									Marks-05

(a) Fill in the blanks								Marks-02

(i)	The electro chemical process in which liquid under go chemical de-	compositon as a result  of passage of electric  current is called Electrolyte.

(ii)	The process by which a current is drawn from an accumulator is called discharge

(b) Write Short Note								Marks-03

(i)	How many types of charging.

There are six types of charging

(aa) 	Initial charge 		(ad) 	Trickle  charge

(ab)	 Float charge 		(ae)	Gases charge

(ac)	 Normal charge 	(af)	Fresh charge.

9.	Construction of line maintenance						Marks-05

(a) Fill In The blanks							Marks-03

(i)	In JWD wire consists of Steel Wire.

(ii)	50000 channels can be carried in half inch diameter fiber optic cable

(iii)	Carrier quad are Two pair lines.

(b) Write Short Note     							Marks-02

(i)	What are the essential items used for Adm line maintenance .   	  	     	(aa)	Cutting player 		(ad)	 Millimeter

(ab)	Insulation tape 	(ae)	 Screw driver

(ac)	 Axes 			(af)	Knife